course: CA
exercise: 2
date: 2024-12-05
author: Miko Osak, 2628565

Each part of the exercise has been completed, including the optional task. It compiles successfully and works successfully. The loadxi function was tested by using a modified version of the provided ArraySum example, and the bitwise operation functions were tested using an updated version of ALUrun as well as the using the provided test program.

In the archive there is a folder called ‘Exercise2’. Inside of folder is the status report you are reading as well as ‘Circuits’ and ‘Programs’ folders. You will find the programs I used in ‘./Programs/Sigma16/Core/UserPrograms/’, these are given as assembly code and object code. The circuits I modified during this assessed exercise are found in ‘./Circuits/M1/’

When using ‘M1run.hs’ to test, run ‘boot UserPrograms/TestArray’ for the program with loadxi and ‘boot UserPrograms/TestLogic’ for the program that uses the bitwise operations.

Task 1

My approach to task 1 (creating loadxi) was first to combine the ‘load’ and ‘add’ functions to make loadxi because loadxi was defined as ‘R1 := mem[12ab+R2], R2 := R2+1’ which is a combination of load and add. The only issue was that there was no control signal specifying that the output of the ALU should go to ir_sa instead of ir_d, and this functionality was needed in order to be able to automatically increment the given index register. So I added a signal ctl_rf_da (da = destination a). When this signal is given, it sets ir_d = ir_sa in the datapath.

Below is M1run’s output for all 4 states of loadxi, here are the part where the instructions are executing:

--------------------------------------------------------------------------------
Cycle 53. Running

System control
  reset = 0 cpu = 1 ctl_start = 0

Input/Output
  io_DMA = 0 io_memStore = 0 io_memFetch = 0 io_regFetch = 0
  io_address = 0000 io_data = 0000

Control state
   st_instr_fet = 00 st_dispatch = 00 st_add = 00 st_sub = 00
        st_inv = 00 st_and = 00 st_or = 00 st_xor = 00
        st_mul0 = 00 st_div0 = 00 st_cmp = 00 st_trap0 = 00
        st_lea0 = 00 st_lea1 = 00 st_load0 = 00
       st_load1 = 00 st_load2 = 00 st_store0 = 00 st_store1 = 00
      st_store2 = 00 st_jump0 = 00 st_jump1 = 00 st_jump2 = 00
     st_jumpc00 = 00 st_jumpc01 = 00 st_jumpc02 = 00 st_jumpc10 = 00
     st_jumpc11 = 00 st_jumpc12 = 00 st_jal0 = 00 st_jal1 = 00
        st_jal2 = 00 st_loadxi0 = 11 st_loadxi1 = 00 st_loadxi2 = 00
     st_loadxi3 = 00

Control signals
      ctl_alu_a = 0 ctl_alu_b = 0 ctl_alu_c = 1 ctl_alu_d = 1
       ctl_x_pc = 1 ctl_y_ad = 0 ctl_rf_ld = 0 ctl_rf_ldcc = 0
      ctl_rf_pc = 0 ctl_pc_ld = 0 ctl_pc_ad = 0 ctl_rf_alu = 0
      ctl_rf_sd = 0 ctl_rf_da = 0 ctl_ir_ld = 0 ctl_pc_ld = 1
      ctl_ad_ld = 1 ctl_ad_alu = 0 ctl_ma_pc = 1 ctl_sto = 0

ALU
  ALU inputs: operation = 0011 x = 000a y = 0000 cc = 0018 ir_d = 5
  ALU outputs: r = 000b ccnew = 0003 condcc = 0

Datapath
      ir = f537 pc = 000a ad = 000f cc = 0018
       a = 0000 b = 0000 x = 000a y = 0000
       p = 0014 q = 000b r = 000b
      ma = 000a md = 0000

Memory
    m_sto = 0 m_addr = 000a m_real_addr = 000a m_data = 0000 m_out = 0014
M1>

--------------------------------------------------------------------------------
Cycle 54. Running

System control
  reset = 0 cpu = 1 ctl_start = 0

Input/Output
  io_DMA = 0 io_memStore = 0 io_memFetch = 0 io_regFetch = 0
  io_address = 0000 io_data = 0000

Control state
   st_instr_fet = 00 st_dispatch = 00 st_add = 00 st_sub = 00
        st_inv = 00 st_and = 00 st_or = 00 st_xor = 00
        st_mul0 = 00 st_div0 = 00 st_cmp = 00 st_trap0 = 00
        st_lea0 = 00 st_lea1 = 00 st_load0 = 00
       st_load1 = 00 st_load2 = 00 st_store0 = 00 st_store1 = 00
      st_store2 = 00 st_jump0 = 00 st_jump1 = 00 st_jump2 = 00
     st_jumpc00 = 00 st_jumpc01 = 00 st_jumpc02 = 00 st_jumpc10 = 00
     st_jumpc11 = 00 st_jumpc12 = 00 st_jal0 = 00 st_jal1 = 00
        st_jal2 = 00 st_loadxi0 = 00 st_loadxi1 = 11 st_loadxi2 = 00
     st_loadxi3 = 00

Control signals
      ctl_alu_a = 0 ctl_alu_b = 0 ctl_alu_c = 0 ctl_alu_d = 0
       ctl_x_pc = 0 ctl_y_ad = 1 ctl_rf_ld = 0 ctl_rf_ldcc = 0
      ctl_rf_pc = 0 ctl_pc_ld = 0 ctl_pc_ad = 0 ctl_rf_alu = 0
      ctl_rf_sd = 0 ctl_rf_da = 0 ctl_ir_ld = 0 ctl_pc_ld = 0
      ctl_ad_ld = 1 ctl_ad_alu = 1 ctl_ma_pc = 0 ctl_sto = 0

ALU
  ALU inputs: operation = 0000 x = 0000 y = 0014 cc = 0018 ir_d = 5
  ALU outputs: r = 0014 ccnew = 0003 condcc = 0

Datapath
      ir = f537 pc = 000b ad = 0014 cc = 0018
       a = 0000 b = 0000 x = 0000 y = 0014
       p = 0012 q = 0014 r = 0014
      ma = 0014 md = 0000

Memory
    m_sto = 0 m_addr = 0014 m_real_addr = 0014 m_data = 0000 m_out = 0012
*** Fetched displacement = 0014
M1>

--------------------------------------------------------------------------------
Cycle 55. Running

System control
  reset = 0 cpu = 1 ctl_start = 0

Input/Output
  io_DMA = 0 io_memStore = 0 io_memFetch = 0 io_regFetch = 0
  io_address = 0000 io_data = 0000

Control state
   st_instr_fet = 00 st_dispatch = 00 st_add = 00 st_sub = 00
        st_inv = 00 st_and = 00 st_or = 00 st_xor = 00
        st_mul0 = 00 st_div0 = 00 st_cmp = 00 st_trap0 = 00
        st_lea0 = 00 st_lea1 = 00 st_load0 = 00
       st_load1 = 00 st_load2 = 00 st_store0 = 00 st_store1 = 00
      st_store2 = 00 st_jump0 = 00 st_jump1 = 00 st_jump2 = 00
     st_jumpc00 = 00 st_jumpc01 = 00 st_jumpc02 = 00 st_jumpc10 = 00
     st_jumpc11 = 00 st_jumpc12 = 00 st_jal0 = 00 st_jal1 = 00
        st_jal2 = 00 st_loadxi0 = 00 st_loadxi1 = 00 st_loadxi2 = 11
     st_loadxi3 = 00

Control signals
      ctl_alu_a = 0 ctl_alu_b = 0 ctl_alu_c = 0 ctl_alu_d = 0
       ctl_x_pc = 0 ctl_y_ad = 0 ctl_rf_ld = 1 ctl_rf_ldcc = 0
      ctl_rf_pc = 0 ctl_pc_ld = 0 ctl_pc_ad = 0 ctl_rf_alu = 0
      ctl_rf_sd = 0 ctl_rf_da = 0 ctl_ir_ld = 0 ctl_pc_ld = 0
      ctl_ad_ld = 0 ctl_ad_alu = 0 ctl_ma_pc = 0 ctl_sto = 0

ALU
  ALU inputs: operation = 0000 x = 0000 y = 0000 cc = 0018 ir_d = 5
  ALU outputs: r = 0000 ccnew = 0004 condcc = 0

Datapath
      ir = f537 pc = 000b ad = 0014 cc = 0018
       a = 0000 b = 0000 x = 0000 y = 0000
       p = 0012 q = 0000 r = 0000
      ma = 0014 md = 0000

Memory
    m_sto = 0 m_addr = 0014 m_real_addr = 0014 m_data = 0000 m_out = 0012
Register file update: R5 := 0012
M1>

--------------------------------------------------------------------------------
Cycle 56. Running

System control
  reset = 0 cpu = 1 ctl_start = 1

Input/Output
  io_DMA = 0 io_memStore = 0 io_memFetch = 0 io_regFetch = 0
  io_address = 0000 io_data = 0000

Control state
   st_instr_fet = 00 st_dispatch = 00 st_add = 00 st_sub = 00
        st_inv = 00 st_and = 00 st_or = 00 st_xor = 00
        st_mul0 = 00 st_div0 = 00 st_cmp = 00 st_trap0 = 00
        st_lea0 = 00 st_lea1 = 00 st_load0 = 00
       st_load1 = 00 st_load2 = 00 st_store0 = 00 st_store1 = 00
      st_store2 = 00 st_jump0 = 00 st_jump1 = 00 st_jump2 = 00
     st_jumpc00 = 00 st_jumpc01 = 00 st_jumpc02 = 00 st_jumpc10 = 00
     st_jumpc11 = 00 st_jumpc12 = 00 st_jal0 = 00 st_jal1 = 00
        st_jal2 = 00 st_loadxi0 = 00 st_loadxi1 = 00 st_loadxi2 = 00
     st_loadxi3 = 11

Control signals
      ctl_alu_a = 0 ctl_alu_b = 0 ctl_alu_c = 1 ctl_alu_d = 1
       ctl_x_pc = 0 ctl_y_ad = 0 ctl_rf_ld = 1 ctl_rf_ldcc = 1
      ctl_rf_pc = 0 ctl_pc_ld = 0 ctl_pc_ad = 0 ctl_rf_alu = 1
      ctl_rf_sd = 0 ctl_rf_da = 1 ctl_ir_ld = 0 ctl_pc_ld = 0
      ctl_ad_ld = 0 ctl_ad_alu = 0 ctl_ma_pc = 0 ctl_sto = 0

ALU
  ALU inputs: operation = 0011 x = 0000 y = 0000 cc = 0018 ir_d = 5
  ALU outputs: r = 0001 ccnew = 0003 condcc = 0

Datapath
      ir = f537 pc = 000b ad = 0014 cc = 0018
       a = 0000 b = 0000 x = 0000 y = 0000
       p = 0001 q = 0001 r = 0001
      ma = 0014 md = 0000

Memory
    m_sto = 0 m_addr = 0014 m_real_addr = 0014 m_data = 0000 m_out = 0012
Register file update: R3 := 0001

************************************************************************
Executed instruction: loadxi R5,0014[R3]
R5 := 0012 was loaded in cycle 55
R3 := 0001 was loaded in cycle 56
Processor state: pc = 000b ir = f537 ad = 0014
************************************************************************
M1>

Task 2

For task 2, I first focused on adding functionality to the ALU. The ability to inverse a word of bits was already implemented in Hydra in ‘Hydra-3.5.7/src/HDL/Hydra/Circuits/Combinational.hs’ as invw. Using that as a guide, I created bitwise operations for words using map2 (and2w, or2w and xor2w).

The ALU has a 3-bit opcode and already supports 5 operations. A 3-bit opcode can only support up to 8 operations. So to add 4 (total 9), I had to add an opcode, resulting in a 4-bit opcode. With this I can have each logic operation have an opcode which has a leftmost bit of 1. And so, INV = 1000, AND = 1001, OR = 1010 and XOR = 1011. Based off the two rightmost values I can see what the exact operation is. Then I can pick whether to return the arithmetic or logic result based off the leftmost bit. I then tested this using ALUrun.

The rest of the task consisted of adding the ctl_alu_d control signal and adding the inv, and, or & xor instructions (similar to task 1). After updating M1run and running the provided program, here are the part where the instructions are executing:

--------------------------------------------------------------------------------
Cycle 21. Running

System control
  reset = 0 cpu = 1 ctl_start = 1

Input/Output
  io_DMA = 0 io_memStore = 0 io_memFetch = 0 io_regFetch = 0
  io_address = 0000 io_data = 0000

Control state
   st_instr_fet = 00 st_dispatch = 00 st_add = 00 st_sub = 00
        st_inv = 11 st_and = 00 st_or = 00 st_xor = 00
        st_mul0 = 00 st_div0 = 00 st_cmp = 00 st_trap0 = 00
        st_lea0 = 00 st_lea1 = 00 st_load0 = 00
       st_load1 = 00 st_load2 = 00 st_store0 = 00 st_store1 = 00
      st_store2 = 00 st_jump0 = 00 st_jump1 = 00 st_jump2 = 00
     st_jumpc00 = 00 st_jumpc01 = 00 st_jumpc02 = 00 st_jumpc10 = 00
     st_jumpc11 = 00 st_jumpc12 = 00 st_jal0 = 00 st_jal1 = 00
        st_jal2 = 00 st_loadxi0 = 00 st_loadxi1 = 00 st_loadxi2 = 00
     st_loadxi3 = 00

Control signals
      ctl_alu_a = 1 ctl_alu_b = 0 ctl_alu_c = 0 ctl_alu_d = 0
       ctl_x_pc = 0 ctl_y_ad = 0 ctl_rf_ld = 1 ctl_rf_ldcc = 0
      ctl_rf_pc = 0 ctl_pc_ld = 0 ctl_pc_ad = 0 ctl_rf_alu = 1
      ctl_rf_sd = 0 ctl_rf_da = 0 ctl_ir_ld = 0 ctl_pc_ld = 0
      ctl_ad_ld = 0 ctl_ad_alu = 0 ctl_ma_pc = 0 ctl_sto = 0

ALU
  ALU inputs: operation = 1000 x = 0003 y = 0005 cc = 0000 ir_d = 3
  ALU outputs: r = fffc ccnew = 0018 condcc = 0

Datapath
      ir = 5312 pc = 0005 ad = 6412 cc = 0000
       a = 0003 b = 0005 x = 0003 y = 0005
       p = fffc q = fffc r = fffc
      ma = 6412 md = 0003

Memory
    m_sto = 0 m_addr = 6412 m_real_addr = 6412 m_data = 0003 m_out = 0000
Register file update: R3 := fffc

************************************************************************
Executed instruction: inv R3,0005[R1]
R3 := fffc was loaded in cycle 21
Processor state: pc = 0005 ir = 5312 ad = 6412
************************************************************************
M1>

--------------------------------------------------------------------------------
Cycle 24. Running

System control
  reset = 0 cpu = 1 ctl_start = 1

Input/Output
  io_DMA = 0 io_memStore = 0 io_memFetch = 0 io_regFetch = 0
  io_address = 0000 io_data = 0000

Control state
   st_instr_fet = 00 st_dispatch = 00 st_add = 00 st_sub = 00
        st_inv = 00 st_and = 11 st_or = 00 st_xor = 00
        st_mul0 = 00 st_div0 = 00 st_cmp = 00 st_trap0 = 00
        st_lea0 = 00 st_lea1 = 00 st_load0 = 00
       st_load1 = 00 st_load2 = 00 st_store0 = 00 st_store1 = 00
      st_store2 = 00 st_jump0 = 00 st_jump1 = 00 st_jump2 = 00
     st_jumpc00 = 00 st_jumpc01 = 00 st_jumpc02 = 00 st_jumpc10 = 00
     st_jumpc11 = 00 st_jumpc12 = 00 st_jal0 = 00 st_jal1 = 00
        st_jal2 = 00 st_loadxi0 = 00 st_loadxi1 = 00 st_loadxi2 = 00
     st_loadxi3 = 00

Control signals
      ctl_alu_a = 1 ctl_alu_b = 0 ctl_alu_c = 0 ctl_alu_d = 1
       ctl_x_pc = 0 ctl_y_ad = 0 ctl_rf_ld = 1 ctl_rf_ldcc = 0
      ctl_rf_pc = 0 ctl_pc_ld = 0 ctl_pc_ad = 0 ctl_rf_alu = 1
      ctl_rf_sd = 0 ctl_rf_da = 0 ctl_ir_ld = 0 ctl_pc_ld = 0
      ctl_ad_ld = 0 ctl_ad_alu = 0 ctl_ma_pc = 0 ctl_sto = 0

ALU
  ALU inputs: operation = 1001 x = 0003 y = 0005 cc = 0000 ir_d = 4
  ALU outputs: r = 0001 ccnew = 0018 condcc = 0

Datapath
      ir = 6412 pc = 0006 ad = 6412 cc = 0000
       a = 0003 b = 0005 x = 0003 y = 0005
       p = 0001 q = 0001 r = 0001
      ma = 6412 md = 0003

Memory
    m_sto = 0 m_addr = 6412 m_real_addr = 6412 m_data = 0003 m_out = 0000
Register file update: R4 := 0001

************************************************************************
Executed instruction: and R4,0005[R1]
R4 := 0001 was loaded in cycle 24
Processor state: pc = 0006 ir = 6412 ad = 6412
************************************************************************
M1>

--------------------------------------------------------------------------------
Cycle 27. Running

System control
  reset = 0 cpu = 1 ctl_start = 1

Input/Output
  io_DMA = 0 io_memStore = 0 io_memFetch = 0 io_regFetch = 0
  io_address = 0000 io_data = 0000

Control state
   st_instr_fet = 00 st_dispatch = 00 st_add = 00 st_sub = 00
        st_inv = 00 st_and = 00 st_or = 11 st_xor = 00
        st_mul0 = 00 st_div0 = 00 st_cmp = 00 st_trap0 = 00
        st_lea0 = 00 st_lea1 = 00 st_load0 = 00
       st_load1 = 00 st_load2 = 00 st_store0 = 00 st_store1 = 00
      st_store2 = 00 st_jump0 = 00 st_jump1 = 00 st_jump2 = 00
     st_jumpc00 = 00 st_jumpc01 = 00 st_jumpc02 = 00 st_jumpc10 = 00
     st_jumpc11 = 00 st_jumpc12 = 00 st_jal0 = 00 st_jal1 = 00
        st_jal2 = 00 st_loadxi0 = 00 st_loadxi1 = 00 st_loadxi2 = 00
     st_loadxi3 = 00

Control signals
      ctl_alu_a = 1 ctl_alu_b = 0 ctl_alu_c = 1 ctl_alu_d = 0
       ctl_x_pc = 0 ctl_y_ad = 0 ctl_rf_ld = 1 ctl_rf_ldcc = 0
      ctl_rf_pc = 0 ctl_pc_ld = 0 ctl_pc_ad = 0 ctl_rf_alu = 1
      ctl_rf_sd = 0 ctl_rf_da = 0 ctl_ir_ld = 0 ctl_pc_ld = 0
      ctl_ad_ld = 0 ctl_ad_alu = 0 ctl_ma_pc = 0 ctl_sto = 0

ALU
  ALU inputs: operation = 1010 x = 0003 y = 0005 cc = 0000 ir_d = 5
  ALU outputs: r = 0007 ccnew = 0018 condcc = 0

Datapath
      ir = 7512 pc = 0007 ad = 6412 cc = 0000
       a = 0003 b = 0005 x = 0003 y = 0005
       p = 0007 q = 0007 r = 0007
      ma = 6412 md = 0003

Memory
    m_sto = 0 m_addr = 6412 m_real_addr = 6412 m_data = 0003 m_out = 0000
Register file update: R5 := 0007

************************************************************************
Executed instruction: or R5,0005[R1]
R5 := 0007 was loaded in cycle 27
Processor state: pc = 0007 ir = 7512 ad = 6412
************************************************************************
M1>

--------------------------------------------------------------------------------
Cycle 30. Running

System control
  reset = 0 cpu = 1 ctl_start = 1

Input/Output
  io_DMA = 0 io_memStore = 0 io_memFetch = 0 io_regFetch = 0
  io_address = 0000 io_data = 0000

Control state
   st_instr_fet = 00 st_dispatch = 00 st_add = 00 st_sub = 00
        st_inv = 00 st_and = 00 st_or = 00 st_xor = 11
        st_mul0 = 00 st_div0 = 00 st_cmp = 00 st_trap0 = 00
        st_lea0 = 00 st_lea1 = 00 st_load0 = 00
       st_load1 = 00 st_load2 = 00 st_store0 = 00 st_store1 = 00
      st_store2 = 00 st_jump0 = 00 st_jump1 = 00 st_jump2 = 00
     st_jumpc00 = 00 st_jumpc01 = 00 st_jumpc02 = 00 st_jumpc10 = 00
     st_jumpc11 = 00 st_jumpc12 = 00 st_jal0 = 00 st_jal1 = 00
        st_jal2 = 00 st_loadxi0 = 00 st_loadxi1 = 00 st_loadxi2 = 00
     st_loadxi3 = 00

Control signals
      ctl_alu_a = 1 ctl_alu_b = 0 ctl_alu_c = 1 ctl_alu_d = 1
       ctl_x_pc = 0 ctl_y_ad = 0 ctl_rf_ld = 1 ctl_rf_ldcc = 0
      ctl_rf_pc = 0 ctl_pc_ld = 0 ctl_pc_ad = 0 ctl_rf_alu = 1
      ctl_rf_sd = 0 ctl_rf_da = 0 ctl_ir_ld = 0 ctl_pc_ld = 0
      ctl_ad_ld = 0 ctl_ad_alu = 0 ctl_ma_pc = 0 ctl_sto = 0

ALU
  ALU inputs: operation = 1011 x = 0003 y = 0005 cc = 0000 ir_d = 6
  ALU outputs: r = 0006 ccnew = 0018 condcc = 0

Datapath
      ir = 8612 pc = 0008 ad = 6412 cc = 0000
       a = 0003 b = 0005 x = 0003 y = 0005
       p = 0006 q = 0006 r = 0006
      ma = 6412 md = 0003

Memory
    m_sto = 0 m_addr = 6412 m_real_addr = 6412 m_data = 0003 m_out = 0000
Register file update: R6 := 0006

************************************************************************
Executed instruction: xor R6,0005[R1]
R6 := 0006 was loaded in cycle 30
Processor state: pc = 0008 ir = 8612 ad = 6412
************************************************************************
M1>